# FAN COIL UNITS 1.5-5TONS

# AHP,SHP

# DESCRIPTION

This fan coil line offers the ultimate in application flexibility. The AHP (non-variable speed motor) models can be ordered upflow only or as multi-position. The multi-position model can be installed in downflow, upflow, and horizontal right or left without the need for additional field installed kits. The SHP 48 & 60 models are upflow only models designed into a shorter cabinet than the AHP version, for those special applications where reduced height is required. All UPG air handlers and coils utilize a TXV to provide our customers with the optimum performance and refrigerant control required for 13+ systems. Air handlers can be ordered with a R22 TXV factory installed that can be easily converted to R410A by changing the bolt-on TXV. Air handlers are also available with “Flex-coils” without a factory-installed metering device. For added flexibility, an R22 or R410A TXV can be field installed to meet your refrigerant choice.

# FEATURES

Thermal Expansion Valve - Provides the ultimate refrigerantcontrol required for today’s high efficient product. The UPG bolt-on TXV provides the added flexibility to convert the air handler to the required refrigerant. The UPG TXV is a truebolt-on which does not require brazing to replace or install. MicroBlueTM Coated Fins - All air handler coils are treated with the MicroBlueTM hydrophilic coating to enhance the removal of condensate during the refrigeration cycle and reduce the possibility of water blow-off. The MicroBlueTM coating also reduces the growth of germ causing microbes for a healthier home environment. Insulated Cabinet - All air handler cabinets are thermally insulated with 1” foil faced insulation (R-4.2) to prevent sweating. For applications in extreme humidity conditions an optional, field installed, external insulating wrap kit is also available. Durable Finish Inside and Out - Air handler casings are made of pre-painted galvanized steel which provides a better paint to steel bond that resists corrosion and rust creep. All internal coil sheet metal parts are made of G90 pre-painted steel (i.e. triangular plates, top plates, horizontal supports, etc). Coil header plates are not painted due to the brazing process during production. The coil header plates are treated after the brazing process with a corrosion resistant spray to reduce the probability of rust. High Efficiency - 5 ton unit has high efficiency DC motor. New 4 HK Heat Kit - Installation friendly, easy service, more robust, unique to new design.