YP9C 98% FURNACE MODULATING GAS WITH VARIABLE SPEED FAN

DESCRIPTION

These compact units employ induced combustion, reliable hot surface ignition and high heat transfer aluminized tubular heat exchangers. The units are factory shipped for installation in upflow or horizontal applications and may be converted for downflow applications. These furnaces are designed for residential installation in a basement, closet, alcove, attic, recreation room or garage and are also ideal for commercial applications. All units are factory assembled, wired and tested to assure safe depend-able and economical installation and operation. These units are Category IV listed and may be vented either through side wall or roof applications using approved plastic combustion air and vent piping.

WARRANTY

Lifetime limited warranty on both heat exchangers to the original purchaser; a 20-year limited warranty from original installation date to subsequent purchaser.10-year warranty on the heat exchanger in commercial appli-cations.5-year limited parts warranty.

FEATURES

•Modulating heating operation includes:- Modulating gas valve, inducer and circulating blower- Modulating operation from 100% input to 35% input in 1% increments

•Easily applied in upflow, horizontal left or right, or downflow installation with minimal conversion necessary.

•Compact, easy to install, ideal height 33" tall cabinet.

•ECM variable speed motor for cooling SEER enhancement and continuous fan options for IAQ performance.

•Easy access to controls to connect power/control wiring.

•Built-in, high level self diagnostics with fault code display.

•Low unit amp requirement for easy replacement application.

•All models are convertible to use propane (LP) gas.

•Electronic Hot Surface Ignition saves fuel cost with increased dependability and reliability.

•100% shut off main gas valve for extra safety.

•24V, 40 VA control transformer and blower relay supplied for add-on cooling.

•Hi-tech tubular aluminized steel primary heat exchanger.

•Blower door safety switch.

•Solid removable bottom panel allows easy conversion.

•Airflow leakage less than 1% of nominal airflow for duct blaster conditions.

•No knockouts to deal with, making installation easier.

•Movable duct connector flanges for application flexibility.

•Quiet inducer operation.

•Inducer rotates for easy conversion of venting options.

•Fully supported blower assembly for easy access and removal of blower.

•External air filters used for maximum flexibility in meeting customers IAQ needs.

•Venting applications - may be installed as a common vent with other gas-fired appliances.

•Insulated blower compartment for quiet operation.

•1/4 turn knobs provided for easy door removal.